## Slide 1: Trusted Computing in OVAL
Charles Schmidt
March 24, 2011

## Slide 2: What is Trusted Computing?
A trusted platform contains hardware-rooted subsystem devoted to maintaining trust & security
Three important roots
  Measurement: Reliably gathering data
  Storage: Securely store data (including TPM), data tampering detectable
  Reporting: Reports data in a verifiable and trustworthy way
New hardware:
  The Trusted Platform Module (TPM)
    Secure storage and reporting, dirt cheap
  “Trusted hardware extensions” (TXT, SVM)
    Flexible root of trust for measurement

## Slide 3: The TPM Itself
I/O
Execution
Storage
Security Enablement
Non-Volatile Secure Storage
Secure Platform Configuration Registers
(PCRs)
Opt-In
(Off by Default)
TPM Processor
Key Generation
Crypto Algorithms
Random Number Generation
Keys (EK, SRK, etc.)

## Slide 4: The TPM: What it Can Do
Secure Storage: Two kinds
  Tiny amounts of measurement data in PCRs
  Key material used to encrypt larger amounts of on-disk data
  Crucial capability: TPM residence of PCR data and storage root key
Secure Reporting
  Quote – PCR values signed by the TPM’s core identity key
  TPM’s core identity key never leaves the chip
    Forms the root of a key hierarchy for reporting
  PCR contents cannot be written arbitrarily
    Final value a combination of multiple hashes from boot
Limited cryptographic operations

## Slide 5: Trusted Computing Paradigm
Final
Enterprise
Reporting
Report-Checking
Server
TPM-based Reports (Quotes)

## Slide 6: Merge OVAL and TPM procedures
Compatible paradigms:
  Collect measurements from hosts
  Evaluate measurements against criteria to determine “compliance”
Two benefits identified
  use security automation standards for the collection and transport of attestation data
  use attestation to provide a root of trust to existing uses of security automation standards

## Slide 7: Using Standards to Improve TPM Paradigm
Quote transport protocols are still under active development
  Several proposals, but nothing that is universally accepted
  Propose something we can use them effectively within our existing SCAP infrastructures
TPM measurements in quotes lack granularity
  PCRs are hashes of multiple measurements – virtually impossible to trace a bad hash to a single cause
  OVAL measurements tell us what went wrong
Goal of the new OVAL TPM Probe
  Identify and transmit useful information about the TPM itself
  Do this in conjunction with the regular, granular OVAL assessments

## Slide 8: Using TPMs to Improve OVAL Operation
Currently
  OVAL can evaluate a vast array of settings on many platforms
  However, OVAL evaluations have no trusted base
    Only as trustworthy as the software OVAL interpreter + libraries
Attesting to correctness of the OVAL interpreter allows us to trust OVAL measurements
  The core of an OVAL interpreters is stateless (between evaluations) and can be quite small
The TPM allows OVAL assessments themselves to be rooted in the hardware of the assessed system
This is slightly different from the current OVAL paradigm
  Quote information not evaluated by OVAL interpreter because it requires special operations (signature verification, etc.)
  Instead, TPM quote’s SC Item acts as a certification of the correct operation of the OVAL infrastructure

## Slide 9: The New TPM Component Schema
quotereport_test
  Purpose is to collect a TPM quote
  Most fields cannot be usefully evaluated in OVAL; full evaluation of the quote results would need to take place externally using the information in the OVAL System Characteristics file
    mask, aikblob, nonce, quotetype – required input to retrieve a quote
    pcr, locality – measurements returned in a quote
    signature, pcrcomposite – data structures provided in a quote for integrity
tpminfo_test
  Test inherent characteristics of a TPM chip
    version, revision, errata_number, manufacturer, manufacturer_info, command_support_level, pcr_count, pcr_attributes, buffer_size

## Slide 10: Demonstration Architecture
Server
Server Controller
XCCDF Interpreter
Client
Client Controller
OVAL DI
TPM-enabled System Measurement
TPM
XCCDF Interp – Processes policies
Server Controller – Orchestrates interactions between OVAL DI, XCCDF Interp., and client
Measurement – Measures system, including OVAL DI
OVAL DI – Collects/evaluates findings
Client Controller – Orchestrate between server and local OVAL DI

## Slide 11: Demonstration Architecture
Server
Server Controller
Results
XCCDF Interpreter
1
3
7
8
Client
Client Controller
OVAL DI
TPM-enabled System Measurement
TPM
4
5
6
a
2
8
The results file is sent to the Client Controller…
… forwarded to the Server Controller, which performs integrity checks
The Server Controller shares passes results tothe XCCDF Interp. to get the configuration results and also stores raw results
Server Controller initiates assessment
XCCDF Interp. processes the guidance and collects OVAL Definitions
Definitions sent to the Client Controller…
… which passes them to the Client OVAL DI
OVAL DI collects system findings, including a TPM quote, and evaluates to produce results, as normal

## Slide 12: Demo status
Current status
  Dynamically insert TPM query definition into OVAL files
    Can be done starting with XCCDF or raw OVAL
  Collect TPM data and store in OVAL results
    Specifically, in the system-characteristics part of the results
  Use collected data to verify integrity of the data
    Ensure quote itself has not been tampered with
Next step
  Insert measurements of OVAL Interpreter into TPM
  Verify those measurements on the server

## Slide 13: Questions for the Community
Is this new capability useful?
  Would vendors be interested in having TPM measurements of their assessment engines?
  Is OVAL the correct way to retrieve this information?
    We are using OVAL to task and transport quotes, but processing is still external to OVAL
What other TPM data to collect?
  Quote collects measurements
  Other probes could collect configuration and capabilities of a TPM
    TPM enabled or disabled
    TPM provisioned or in factory default
    Manufacturer, build set, manufacturer custom strings
    Characteristics of the chip (IO speed, number of registers, etc.)
    TPM device driver version and support level

## Slide 14
Questions?

## Slide 15: quotereport_test
Object
<xsd:extension base="oval-def:ObjectType"> <xsd:sequence> <xsd:element name="mask" type="oval-def:EntityObjectIntType" minOccurs="1" maxOccurs="unbounded"/> <xsd:element name="quotetype" type="tpm-def:EntityObjectQuotetypeType" minOccurs="1" maxOccurs="1"/> <xsd:element name="aikblob" type="oval-def:EntityObjectBinaryType" minOccurs="1" maxOccurs="1"/> <xsd:element name="nonce" type="oval-def:EntityObjectBinaryType" minOccurs="1" maxOccurs="1"/> </xsd:sequence> </xsd:extension>
State
<xsd:extension base="oval-def:StateType"> <xsd:sequence> <xsd:element name="mask" type="oval-def:EntityStateIntType" minOccurs="0" maxOccurs="unbounded"/> <xsd:element name="aikblob" type="oval-def:EntityStateBinaryType" minOccurs="0" maxOccurs="1"/> <xsd:element name="nonce" type="oval-def:EntityStateBinaryType" minOccurs="0" maxOccurs="1"/> <xsd:element name="quotetype" type="tpm-def:EntityStateQuotetypeType" minOccurs="0" maxOccurs="1"/> <xsd:element name="signature" type="oval-def:EntityStateBinaryType" minOccurs="0" maxOccurs="1"/> <xsd:element name="pcr" type="oval-def:EntityStateRecordType" minOccurs="0" maxOccurs="1"/> <xsd:element name="pcrcomposite" type="oval-def:EntityStateBinaryType" minOccurs="0" maxOccurs="1"/> <xsd:element name="locality" type="oval-def:EntityStateIntType" minOccurs="0" maxOccurs="1"/> </xsd:sequence> </xsd:extension>

## Slide 16: tpminfo_test
State
<xsd:extension base="oval-def:StateType"> <xsd:sequence> <xsd:element name="version" type="oval-def:EntityStateVersionType" minOccurs="0" maxOccurs="1"/> <xsd:element name="revision" type="oval-def:EntityStateVersionType" minOccurs="0" maxOccurs="1"/> <xsd:element name="errata_number" type="oval-def:EntityStateIntType" minOccurs="0" maxOccurs="1"/> <xsd:element name="manufacturer" type="oval-def:EntityStateBinaryType" minOccurs="0" maxOccurs="1"/> <xsd:element name="manufacturer_info" type="oval-def:EntityStateBinaryType" minOccurs="0" maxOccurs="1"/> <xsd:element name="command_support_level" type="oval-def:EntityStateBinaryType" minOccurs="0" maxOccurs="1"/> <xsd:element name="pcr_count" type="oval-def:EntityStateIntType" minOccurs="0" maxOccurs="1"/> <xsd:element name="pcr_attributes" type="oval-def:EntityStateBinaryType" minOccurs="0" maxOccurs="1"/> <xsd:element name="buffer_size" type="oval-def:EntityStateIntType" minOccurs="0" maxOccurs="1"/> </xsd:sequence> </xsd:extension>